## Slide 1: STOL 항공기의 공력 및 성능 연구
박세환
한화에어로스페이스

## Slide 2: Introduction
Blown-Lift Wing
  NASA X-57 Maxwell
    Leading Edge Asynchronous Propeller (LEAP) Technology
  Electra Aero
    Ultra STOL Aircraft with 150 ft Ground Roll

## Slide 3: Introduction
Short Takeoff and Landing (STOL)
  Gray Eagle 25M
    200-HP Heavy Fuel Engine 2.0
    Maximum Gross Takeoff Weight: 4,200 lb
    Maximum airspeed: 167 kts
  Mojave STOL
    Rolls Royce M250 (450 SHP)
    Maximum Gross Takeoff Weight: 7,000 lb
    Maximum airspeed: 140 kts
    Takeoff Distance: 400 – 1,000 ft

## Slide 4: Aerodynamic Modeling
Wing Modeling
  Vortex Lattice Method
  Flap/Aileron Surface Deflected
Wake Modeling
  Free-wake
  Constant Vorticity Contour Wake Model
Automation
  OpenVSP-to-CHARM process
  CHARM Run/Post-Process
OpenVSP Model
CHARM Model

## Slide 5: Aerodynamics Analysis
Blown-Lift Effect
CaseID |  | Small Prop | Large Prop | delta CL | CL Multiplier
000 | Flap 0 deg, Aileron 0 deg | - | - | -0.66 | 0.60
001 | Flap 30 deg, Aileron 10 deg | - | - | - | 1.00
002 |  | Inboard/Outboard | - | 0.12 | 1.07
003 |  | Inboard | - | 0.10 | 1.06
004 |  | Outboard | - | 0.00 | 1.00
005 |  | - | Inboard/Outboard | 0.59 | 1.36
006 |  | - | Inboard | 0.46 | 1.28
007 |  | - | Outboard | 0.18 | 1.11
Chart: y/b
| 0.20910000000000001 | 0.3 | 0.39090000000000003 | 0.5 | 0.6 | 0.70179999999999998 | 0.80359999999999998 | 0.90549999999999997 | 0.94910000000000005 | 0.99270000000000003
Case002 | 0.011235 | 0.011882 | 0.011954 | 0.011556 | 0.0095383 | 0.0063956 | 0.0048477 | 0.0033154 | 0.0022288 | 0.0022288
Case004 | 0.013179 | 0.014656 | 0.020626 | 0.013252 | 0.0099298 | 0.0060913 | 0.0048351 | 0.0034152 | 0.0023164 | 0.0023164
Case001 | 0.0033849 | 0.0035044 | 0.0035316 | 0.0035039 | 0.0033515 | 0.0031488 | 0.0028008 | 0.0021294 | 0.0014962 | 0.0014962

## Slide 6: Takeoff Performance
Ground Roll Distance
Airborne Distance
  Transition
  Remaining Climb
Source: Pamadi, B., Performance, Stability, Dynamics, and Control of Airplanes, 2015
horizontal transition distance
altitude gained during transition

## Slide 7: Takeoff Performance
Runway Condition
  Unbraked
    Paved Runway: 0.025 for Dry (Source: MIL-STD-3013B)
    Semi-Prepared: 0.040 for Firm Dirt (Source: Raymer, 0.05 for hard turf, 0.04 for firm dirt, 0.07 for soft turf)
    Martime: 0.050 for Wet (Source: MIL-STD-3013B)
Ground Roll Distance
Chart: Takeoff Weight (lb)
| 5000 | 5500 | 6000 | 6500 | 7000
Baseline (Dry) | 460.8745 | 569.871 | 692.4414 | 828.9551 | 979.7035
Blown-Lift (Dry) | 402.8754 | 497.797 | 604.5984 | 723.6824 | 855.4084
Baseline (Firm Dirt) | 474.6171 | 589.1324 | 718.7372 | 864.0579 | 1025.6598
Blown-Lift (Firm Dirt) | 397.9865 | 493.46 | 601.5527 | 722.8839 | 858.0574
Baseline (Wet) | 484.4156 | 602.9916 | 737.8405 | 889.8179 | 1059.7436
Blown-Lift (Wet) | 405.9885 | 504.7482 | 617.0812 | 743.797 | 885.7147
Chart: Takeoff Weight (lb)
| 5000 | 5500 | 6000 | 6500 | 7000
Baseline (Dry) | 460.8745 | 569.871 | 692.4414 | 828.9551 | 979.7035
Blown-Lift (Dry) | 402.8754 | 497.797 | 604.5984 | 723.6824 | 855.4084
250 ft

## Slide 8: Takeoff Performance
Runway Condition
  Unbraked
    Paved runway: 0.025 for Dry (Source: MIL-STD-3013B)
    Semi-prepared: 0.040 for Firm Dirt (Source: Raymer, 0.05 for hard turf, 0.04 for firm dirt, 0.07 for soft turf)
    Martime: 0.050 for Wet (Source: MIL-STD-3013B)
Chart: Takeoff Weight (lb)
| 5000 | 5500 | 6000 | 6500 | 7000
Baseline (Dry) | 1260.8733 | 1437.6029 | 1629.5131 | 1836.787 | 2059.5107
Blown-Lift (Dry) | 1170.632 | 1332.3704 | 1507.584 | 1696.5647 | 1899.5418
Baseline (Firm Dirt) | 1274.6159 | 1456.8643 | 1655.809 | 1871.8898 | 2105.467
Blown-Lift (Firm Dirt) | 1156.4417 | 1318.4441 | 1494.6478 | 1685.58 | 1891.7339
Baseline (Wet) | 1284.4143 | 1470.7235 | 1674.9123 | 1897.6498 | 2139.5508
Blown-Lift (Wet) | 1164.4438 | 1329.7323 | 1510.1763 | 1706.4932 | 1919.3911
50ft Clearnace Takeoff Distance
250 ft

## Slide 9: Takeoff Performance
Altitude Effect
  Variations in air density and engine available power with altitude were considered
    where and
Altitude effect on ground roll distance
Chart: Takeoff Ground Run Distance
| 281.79425405716006 | 302.52784400422087 | 352.60580872872248 | 412.15641050842794
4000 lb (Baseline) | 0 | 2000 | 4000 | 6000
5000 lb (Baseline) | 0 | 2000 | 4000 | 6000
6000 lb (Baseline) | 0 | 2000 | 4000 | 6000
7000 lb (Baseline) | 0 | 2000 | 4000 | 6000
4000 lb (Blown-Lift) | 0 | 2000 | 4000 | 6000
5000 lb (Blown-Lift) | 0 | 2000 | 4000 | 6000
6000 lb (Blown-Lift) | 0 | 2000 | 4000 | 6000
7000 lb (Blown-Lift) | 0 | 2000 | 4000 | 6000
250 ft

## Slide 10: Landing Performance
Landing Distance Analysis
  Numerical integration of deceleration from touchdown to stop
  Aerodynamic drag, wheel braking, rolling resistance, and reverse thrust considered
  Tire–runway friction, brake-force limit, and landing-gear load transfer accounted for
  Runway-condition-dependent friction coefficients applied
Chart: Landing Weight (lb)
| 5000 | 5500 | 6000 | 6500 | 7000
Baseline (Dry) | 1431.7198 | 1574.8918 | 1718.0638 | 1861.2358 | 2004.4077
Blown-Lift (Dry) | 1254.1633 | 1379.5797 | 1504.996 | 1630.4124 | 1755.8287
Baseline (Firm Dirt) | 1526.7273 | 1679.4 | 1832.0728 | 1984.7455 | 2137.4182
Blown-Lift (Firm Dirt) | 1283.4495 | 1411.7945 | 1540.1394 | 1668.4844 | 1796.8294
Baseline (Wet) | 1979.9618 | 2177.958 | 2375.9542 | 2573.9503 | 2771.9465
Blown-Lift (Wet) | 1662.1398 | 1828.3537 | 1994.5677 | 2160.7817 | 2326.9957
Landing Distance
250 ft

## Slide 11: Rejected Takeoff Distance
Rejected Takeoff
  Phase 1 – Acceleration
  Phase 2 – Recognition/Transition
  Phase 3 – Braking
Chart: Takeoff Weight (lb)
| 5000 | 5500 | 6000 | 6500 | 7000
Baseline (Dry) | 4274.5932 | 4781.8216 | 5314.053 | 5875.4716 | 6471.2503
Blown-Lift (Dry) | 4216.8216 | 4710.1341 | 5226.7186 | 5770.9955 | 6348.6649
Baseline (Firm Dirt) | 4422.9252 | 4978.7937 | 5573.738 | 6216.4297 | 6918.4806
Blown-Lift (Firm Dirt) | 4331.9158 | 4865.7589 | 5436.4013 | 6053.6486 | 6731.6269
Baseline (Wet) | 4433.001 | 4993.5907 | 5594.9612 | 6246.2667 | 6959.6935
Blown-Lift (Wet) | 4340.3156 | 4878.0922 | 5454.0956 | 6078.5323 | 6765.9724

## Slide 12: Conclusion
Summary
  High-lift propeller was adopted to increase the maximum lift coefficient
  Blown-lift effects were captured using medium-fidelity aerodynamic simulations
  Predicted blown-lift effects were incorporated into takeoff and landing performance analysis
  Improved low-speed performance demonstrated the potential of distributed high-lift propulsion for STOL operations
Future Works
  Optimization of high-lift propeller location, geometry, and operating conditions
  Wing chord/area reduction leveraging blown lift to improve cruise efficiency and maximum-speed capability
  Assessment of high-lift prop system weight penalty and its impact on overall aircraft performance